## Slide 1: Geotechnical Asset Management Colorado DOT Update
Mark Vessely, P.E., Shannon and Wilson, Inc.
Ty Ortiz, P.E., Colorado Department of Transportation
TRB Geotechnical Asset Management Subcommittee
January 2016

## Slide 2: GMP Inventory
Notes: Mention expert elicitation

## Slide 3: Approach Evolution
  Adapting risk calculations to CDOT/MAP-21 performance areas
    Potential impacts to safety, mobility, maintenance/condition metrics
Fitting the plan into the CDOT TAM models
  Risk aggregation versus separation
  Finding the one performance measure
Challenges with defining sites
Notes: Mention expert elicitation

## Slide 4: CDOT GMP Risk Cost
Cost Based Risk Calculation
  Produces a annual risk cost value for the given asset
  R(safety, mobility, or maintenance) = P(H) x P(S:H) x V(Prop:S)
    Probability of the hazard
      Condition measures converted to probability
    Probability of impact
    Value ($)

## Slide 5: Safety Risk Cost Example
Consequence
  No accidents: $0
  1-2 accidents: $3,500
  3-4 accidents: $10,500
  5-10 accidents/injury: $35,000
  Injury: $91,600
Likelihood:
  Combination of condition scores and AADT
Result = Segment Safety Risk Cost ($)

## Slide 6: Mobility Risk Cost
Consequence
  Negligible: $0
  Minor delay <1hr: 0.5hr x $21/hr x AADT
  Major delay 1-24 hours: 12hr x $21/hr x AADT
  Critical delay 1-5 days: 2 days x 24 hrs x $21/hr x AADT
  Catastrophic >5 days: 5 days x 24 hrs x $21/hr x AADT
  Apply a detour factor for Major to Catastrophic delays
Likelihood:
  Based on condition scores
Result = Segment Mobility Risk Cost ($)
Notes: Note: can consider more variables for greater delay but will increase calculation complexity and may not significantly change outcome

## Slide 7: Maintenance Risk Cost
Consequence to Maintenance
  Incidental <$25K: use $5K
  Minimal $25K-$100K: use $50K
  Major $100K-$500K: use $200K
  Catastrophic >$500K: use $1M
  Costs based on Enterprise Accounting data or other department reports
Likelihood:
  Based on a condition scores
Result = Segment Maintenance Risk Cost ($)

## Slide 8: Aggregation or Separation of Risks
Perform mitigation planning/trade off analysis for each performance area or as a sum of all risks
  Manage only safety, condition, or mobility
  Manage all together
    Equal weighting between performance areas

## Slide 9: Level of Risk Grading
Level of Risk (LOR) – Geotechnical Performance Measure
  A, B, C, D, F Grading based on safety, mobility, and maintenance risk scores
Notes: Mention expert elicitation

## Slide 10: CDOT GMP Level of Risk Metric
A = <$1000
B = $1,000 - $5,000
C = $5,000 - $50,000
D = $50,000 - $100,000
E = >$100,000

## Slide 11: Site versus GMP Segment
Site
  Site – difficulty with accuracy in reporting and measurement (when does one site become another site, e.g. different hazard types or different sites of the same type)
  Challenge when aggregating hazards
Segment
  GMP Segment of 0.1 mile
  Allows for overlapping hazards in same segment (rockfall, rockslide, landslide, avalanche, etc.)
  All events in a segment are summed to determine risk costs for safety, mobility, and maintenance

## Slide 12: Implementing the GMP
Setting Targets
Determining Performance (in a risk based system)
    The affect mitigation has on performance
    Passive
    Active
    Life cycle (deterioration curve)
    Cross Asset Optimization
Want vs Need

## Slide 13
Performance Curve - Bridge
  This looks reasonable. How hard can it be?
Notes: The budgets shown do not include these fixed costs: $50M to the viaduct, $15M for debt service and $10M for inspections. The $165M request for FY17 compares to $89M on this graph (50 + 39).

## Slide 14
Performance Curve - Geohazards
  Well … this doesn’t look good, lets change it!

## Slide 15
Performance Curve - Geohazards
  Hmm …. Maybe now is a good time to ask for more money?
Chart: Percent of Segments At or Above Risk Grade C Fiscally Constrained Target is 80%
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036
Target: 80% | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80
Budget Request: $15M | 77.8467 | 70.6877 | 70.8568 | 70.9696 | 71.0823 | 71.3641 | 71.5896 | 71.8151 | 72.0406 | 72.2661 | 72.4915 | 72.717 | 72.9425 | 73.168 | 73.3371 | 73.5062 | 73.6753 | 73.8444 | 74.0135 | 74.1826 | 74.3517 | 74.5209
Plus 2 Intervals: $11.4M | 77.8467 | 70.6877 | 70.8568 | 70.9696 | 71.0823 | 71.2514 | 71.4205 | 71.5896 | 71.7587 | 71.9278 | 72.097 | 72.2661 | 72.3788 | 72.4915 | 72.6043 | 72.717 | 72.8298 | 72.9425 | 73.0552 | 73.168 | 73.2807 | 73.3935
Plus 1 Interval: $9.9M | 77.8467 | 70.6877 | 70.8568 | 70.9696 | 71.0823 | 71.2514 | 71.3641 | 71.4769 | 71.5896 | 71.7024 | 71.8151 | 71.9278 | 72.0406 | 72.1533 | 72.2661 | 72.3788 | 72.4915 | 72.6043 | 72.717 | 72.8298 | 72.8861 | 72.9425
Planning Budgets: $8.4M | 77.8467 | 70.6877 | 70.8568 | 70.9696 | 71.0823 | 71.195 | 71.3078 | 71.4205 | 71.5333 | 71.646 | 71.7587 | 71.8715 | 71.9278 | 71.9842 | 72.0406 | 72.097 | 72.1533 | 72.2097 | 72.2661 | 72.3224 | 72.3788 | 72.4352
Minus 1 Interval: $6.9M | 77.8467 | 70.6877 | 70.8568 | 70.9696 | 71.0823 | 71.1387 | 71.195 | 71.2514 | 71.3078 | 71.3641 | 71.4205 | 71.4769 | 71.5333 | 71.5896 | 71.646 | 71.7024 | 71.7587 | 71.8151 | 71.8715 | 71.9278 | 71.9842 | 72.0406
Minus 2 Intervals: $5.4M | 77.8467 | 70.6877 | 70.8568 | 70.9696 | 71.0823 | 71.1387 | 71.195 | 71.2514 | 71.3078 | 71.3641 | 71.4205 | 71.4769 | 71.5333 | 71.5333 | 71.5333 | 71.5333 | 71.5333 | 71.5333 | 71.5333 | 71.5333 | 71.5333 | 71.5333

## Slide 16
Want vs. Need

## Slide 17
Should we try to fix this?

## Slide 18
Should we try to stop this?

## Slide 19
Should we try to find these?

## Slide 20
Or should we try to keep this clean?
Notes: 20
Rockfall catchments (ditch). Probably the most common method of protection.
A combination of ditch and a construction a stable cut is the best approach.

## Slide 21
Observations … Questions
How effective is our mitigation?
What is the life cycle of our device?
What is the life cycle for our “asset”. How long does it take a rock cut to deteriorate? It depends isn’t a valid answer for building a curve.
What is a realistic target?

## Slide 22
Drive Safely