## Slide 1: Unstable Slope Management Program (USMP) for Federal Land Management Agencies (FLMA’s)
Eli Cuelho, PE Darren Beckstrand, CPG Dave Stanley, CPG Paul Thompson Douglas A. Anderson, LEG | MSU – Western Transportation Institute Landslide Technology DA Stanley Consulting Consultant FHWA – WFLHD

## Slide 2: Project Partners
Managing Agency
Principal Investigators
Participating Agencies

## Slide 3: Background
Phase 1: FHWA project contracted to AKDOT
  Included adaptation of AKDOT’s USMP for FLMAs with stakeholder input, test ratings, and criteria definitions.
Phase 2: FHWA project subcontracted to WTI
  Consists of 15 tasks
  Scheduled for completion September 2017

## Slide 4: Phase 1 - USMP for FLMA Combined Form

## Slide 5: Phase 1 - Rated Sites

## Slide 6: Phase 2
Task 1 – Performance Measures (LT/DASC)
Tasks 2 & 3 – Initial Database Development (WTI)
Task 4 – Input Phase I Data (WTI/LT)
Task 5 – Site Visits & Conceptual Costs (LT)
Task 6 – Cost-Benefit Alternatives (PDT/LT/DASC)
Tasks 7, 10, 13 – Database, GIS Integration, Searching, Mobile App Development (WTI)
Tasks 8, 9 – Field Manual & Training Tools (LT/WTI)
Tasks 11, 12 – New Forms (Maint. Tracking/New Slope)
Task 14 – Qualitative Risk Analysis Module (NPS)
Task 15 – Tech Deployment & Training Course

## Slide 7: Phase 2
Task 1 – Performance Measures (LT/DASC)
Tasks 2 & 3 – Initial Database Development (WTI)
Task 4 – Input Phase I Data (WTI/LT)
Task 5 – Site Visits & Conceptual Costs (LT)
Task 6 – Cost-Benefit Alternatives (PDT/LT/DASC)
Tasks 7, 10, 13 – Database, GIS Integration, Searching, Mobile App Development (WTI)
Tasks 8, 9 – Field Manual & Training Tools (LT/WTI)
Tasks 11, 12 – New Forms (Maint. Tracking/New Slope)
Task 14 – Qualitative Risk Analysis Module (NPS)
Task 15 – Tech Deployment & Training Course (LT/WTI)

## Slide 8: Performance Measures – USFS
DOTs have Functional Classification, the USFS have 5 Maintenance Levels
  ML-1 are in ‘Storage’
  ML-2 ‘High Clearance Vehicles’
  ML-3 Open & Maintained, comfort/convenience not a priority
  ML-4 Moderate comfort at moderate speeds
  ML-5 High comfort, paved (usually), highest FS standard

## Slide 9: Performance Measures – USFS
Condition Performance Measurement
Management Performance Measurement

## Slide 10: Performance Measures – USFS
Condition Performance Measurement
  Needed to develop management and assessment approach for each ML
 | Mgmt | Assessment | Planned Assessment
ML-1 | Reactionary | Judgment | None, Maint. tracked
ML-2 | Reactionary | Judgment | None, Maint. tracked
ML-3 | Proactive | % G/F/P – 5yr cycle, low goals | Preliminary GAM
ML-4 | Proactive | % G/F/P – 5yr cycle, mod. goals | Detailed GAM
ML-5 | Proactive | % G/F/P – 5yr cycle, high goals | Detailed GAM

## Slide 11: Performance Measures – USFS
Condition Performance Measurement
  Minimum Cond. Lvl. for Route Segments
 | GOOD | FAIR | POOR
ML-1 | Few to no US* | Few/Occ. US (1-2/mi) | Many US
ML-2 | Few to no US, Log haul not impacted | Few/Occ. US | Many US
ML-3 | 80% Good, 10% Poor | 70% Good, 15% Poor | 40% Fair or Poor
ML-4 | 85% Good, 5% Poor | 80% Good, 10% Poor | 30% Fair or Poor
ML-5 | 95% Good, 2% Poor | 90% Good, 4% Poor | 20% Fair or Poor
* Unstable Slopes

## Slide 12: Performance Measures – USFS
Condition Performance Measurement
  Route Closures due to Geotech Failures
 | GOOD | FAIR | POOR
ML-1 | Not Blocked – No Threats | Minor Rehab to open to ML 2 | Major Rehab to open to ML 2
ML-2 | Not Blocked – No Threats | Commonly blocked @ rate of 1 / 5 miles | Commonly blocked @ rate of 1 / 2 miles
ML-3 | 1 closure / 10 mi / 3 yrs | 1 closure / 5 mi / 3 yrs | 1 closure / 5 mi / 1 yr
ML-4 | 1 closure / 15 mi / 3 yrs | 1 closure / 10 mi / 3 yrs | 1 closure / 5 mi / 3 yr
ML-5 | 1 closure / 20 mi / 5 yrs | 1 closure / 10 mi / 5 yrs | 1 closure / 10 mi / 3 yr

## Slide 13: Management Perf. Measures
Goal – Maintain slope condition to applicable Good-Fair-Poor service levels.
 | Previous Period | Current Period | Perf. Target | Trend
ML-1 |  |  | None | 
ML-2 |  |  | Fair | 
ML-3 |  |  | <1 per 3 years per 10 miles | 
ML-4 |  |  | <1 per 3 years per 15 miles | 
ML-5 |  |  | <1 per 5 years per 20 miles | 

## Slide 14: Management Perf. Measures
Goal – Ensure Safety, Mobility, & Reliability
  Limit Closure Times & Track Trends
    6 Mos (ML-1) to 1 day (ML-1)
    Track average times per monitoring period to demonstrate performance

## Slide 15: Management Perf. Measures
Goal – Focus on High Priority Roads for Improvement.
 | Previous Period | Current Period | Perf. Target | Trend
ML-1 |  |  | None | 
ML-2 |  |  | Fair | 
ML-3 |  |  | Avg. Score (prelim) <21 Good | 
ML-4 |  |  | Avg. Score <200, Good | 
ML-5 |  |  | Avg. Score <175, Good | 

## Slide 16: Phase 2
Task 1 – Performance Measures (LT/DASC)
Tasks 2 & 3 – Initial Database Development (WTI)
Task 4 – Input Phase I Data (WTI/LT)
Task 5 – Site Visits & Conceptual Costs (LT)
Task 6 – Cost-Benefit Alternatives (PDT/LT/DASC)
Tasks 7, 10, 13 – Database, GIS Integration, Searching, Mobile App Development (WTI)
Tasks 8, 9 – Field Manual & Training Tools (LT/WTI)
Tasks 11, 12 – New Forms (Maint. Tracking/New Slope)
Task 14 – Qualitative Risk Analysis Module (NPS)
Task 15 – Tech Deployment & Training Course (LT/WTI)

## Slide 17: Cost – Benefit Approach
Most geotech inventories have followed simple approach
  RHRS: Mitigation cost/score ratio (bang for the buck) and worst first
  WSDOT: Mitigation cost w/OH to risk cost (maintenance, life-safety)
TAM approach
  Use M&O, user, and improvement costs to prolong deterioration and justify expenditures

## Slide 18: TAM Approach
Consistent with agency mission & objectives
Objective and consistent through inventory, time, inspectors
Based on reliable data, where possible
Sound engineering and economic reasoning
Tolerant of missing or estimated data
Able to be improved over time

## Slide 19: Four Approaches Formulated
Computed benefits and costs (requires the most data)
Priority index (simpler, more generalized)
USMP score priority index (light data requirements, worst first, doesn’t consider life cycle or user costs)
Hybrid of 1 and 2 (reliable with incomplete database, sound engineering and economic analysis)

## Slide 20: Approach 1 - Example
Project | AADT | Detour Length | Likelihood | Life Cycle | Cost Risk | Benefit | Mit. Cost | BC Ratio
13.26 | 500 | 30 | 0.3 | 8565 | $531k | $168k | $645k | 0.26
21.71 | 100 | 30 | 0.3 | 6231 | $126k | $ 44k | $112k | 0.39
25.11 | 100 | 30 | 1.0 | 8906 | $114k | $124k | $332k | 0.37
24.63 | 100 | 30 | 1.0 | 27074 | $148k | $175k | $545k | 0.32
28.36 | 100 | 30 | 1.0 | 6597 | $111k | $117k | $811k | 0.14

## Slide 21: Phase 2
Task 1 – Performance Measures (LT/DASC)
Tasks 2 & 3 – Initial Database Development (WTI)
Task 4 – Input Phase I Data (WTI/LT)
Task 5 – Site Visits & Conceptual Costs (LT)
Task 6 – Cost-Benefit Alternatives (PDT/LT/DASC)
Tasks 7, 10, 13 – Database, GIS Integration, Searching, Mobile App Development (WTI)
Tasks 8, 9 – Field Manual & Training Tools (LT/WTI)
Tasks 11, 12 – New Forms (Maint. Tracking/New Slope)
Task 14 – Qualitative Risk Analysis Module (NPS)
Task 15 – Tech Deployment & Training Course (LT/WTI)

## Slide 22: Maintenance Tracking Form
Notes: Minimal Questions focused location, maintenance activity, and costs.

## Slide 23: Event Tracking Form
Notes: Minimal Questions focused location, maintenance activity, and costs.

## Slide 24: WTI’s Website

## Slide 27: Questions?

## Slide 28: WTI’s Mobile App